Led is connected to pin 4, SUPER BRIGHT. Use as FLASH (momentary). CAN’T PWM DUE TO POWER ISSUES, will cause module to audibly whine

can control red light on back of module, connected to pin 33, if pin 33 value=1, then light is off

sd card pins:
CLK = 14
CMD = 15
DATA0 = 2
DATA1/flashlight = 4
DATA2 = 12
DATA3 = 13

POWER VIA 5V BUS (LEFT SIDE)

OV2640 CAMERA connections
D0 – GPIO5 – Y2_GPIO_NUM
D1 – GPIO18 – Y3_GPIO_NUM
D2 – GPIO19 – Y4_GPIO_NUM
D3 – GPIO21 – Y5_GPIO_NUM
D4 – GPIO36 – Y6_GPIO_NUM
D5 – GPIO39 – Y7_GPIO_NUM
D6 – GPIO34 – Y8_GPIO_NUM
D7 – GPIO35 – Y9_GPIO_NUM
XCLK – GPIO0 – XCLK_GPIO_NUM
PCLK – GPIO22 – PCLK_GPIO_NUM
VSYNC – GPIO25 – VSYNC_GPIO_NUM
HREF – GPIO23 – HREF_GPIO_NUM
SDA – GPIO26 – SIOD_GPIO_NUM
SCL – GPIO27 – SIOC_GPIO_NUM
POWER PIN – GPIO32 - PWDN_GPIO_NUM